## Slide 1: Target shaft and bearing test
Geunhyeong Lee
07/02/2024

## Slide 2: Test plans
Validation the service temperature of the Inconel shaft
  Inconel service temperature ~ 650 C (Invar ~ 400C)
Validate the service temperature of the bearing
  New bearing service temperature ~ 230 C (Current bearing ~ 150 C)
Understand the thermal behavior of the target by demonstrating a thermal conditions similar to those of the actual system
For the details: N:\songj\2024_target_spindle_offline_test

## Slide 3: Overview
Motor, rotation
Vacuum
Coil, heating
Thermal camera
Thermal camera
Water cooling
Thermocouple

## Slide 4: Experiment procedure
Setup
  Preparing the components
    Base structures (Vacuum chamber, flanges, motor, …)
    Water cooling components
    Coil development
  Assemble the structures
    Assemble the flanges and shaft
    Connected the motor to the vacuum chamber
    by adjusting the height
    Coil assemble
    Water cooling loop system
    Thermal camera and thermocouple
  DAQ system
    Verify the rotational speed (~500 rpm)
    Motor current, temperature (estimate the friction)
    File save
* Color indicate : done

## Slide 5: Experiment procedure
Pre-test
  Vacuum test
    5e-3 torr for 1 hr running
  Rotating test
  Cooling loop test
    Cooling water loop test with flowmeter
  Calibration
    IR camera temperature calibration
      Literature study
      Calibration at the system
Simulation
  Basic thermal simulation
  Current input of coil
  Cooling behavior according to the flowrates
  Variable changes to know the trend of temperatures
Experiment (Plan: during the July)