## Slide 1: LPCS Drift Tube Temperature Comparison
Geunhyeong Lee
10/30/2025

## Slide 2: Introduction
The currently installed LPCS drift tube was analyzed by comparing the experimental data.
The simulation condition was given by Kei (20251020_CSS_spot_fukushima.pptx)
Details are in the appendix
  Appendix1: Material propreties
  Appendix2: Boundary conditions
Other simulation condition details (mesh independent, Gnielinski correction, flow conditions) in the previous calculation (“N:\leeg\Presentation\ LPCS_drift_tube_transient”)

## Slide 3: Variables
The temperature-dependent variables for current analysis
  Power input
    14.5 W
  Beam size
  Beam location
    5 mm, 10 mm, 15 mm from the end of the pipe
  Brazing thickness
    < 15 % difference from previous analysis (340W power deposition)
Beam
20251020_CSS_spot_fukushima.pptx

## Slide 4: Measured point
4 temperature measurement sensors

## Slide 5: Experimental data
Temperature difference measurements
  A1: 2.3 C, A2: 7 C
A2
A1

## Slide 6: Simulation results
Simulation results
  Power change at designated points (5mm, 10 mm, 15 mm from the end of pipe)
0
5 ~ 15 mm
A2 (T = 7 C)
A1 (T = 2.3 C)
Match around 0.6 W

## Slide 7: Simulation results
Temperature distribution
  0.6 W deposited
  10 mm distance from the end of pipe

## Slide 8: Simulation results
Power limitation
  The maximum stress is over the yield strength at 17.2 W
  Water channel temperature < 100 C at this point
17.2 W

## Slide 9: Conclusion
The deposited power for the Oct 17, 2025 case was calculated to be 0.6 W.
The power limitation based on yield strength was 17.2 W.

## Slide 10: Appendix 1: Material properties
Stainless Steel 304 (from MPDB)
Welding material (SILVALOY 721, ~72% silver, ~28% copper)
  Thermal conductivity: 200 W/mK
  Others as silver properties
Young’s Modulus
Poisson’s ratio
Thermal conductivity
Thermal expansion

## Slide 11: Appendix 2: Boundary condition
Turbulent flow ()
  Inlet: 1 gal/min
  Outlet: 0 Pa
Heat transfer
  Inflow temperature: 32 C
  Deposited beam power: Normal to the center of surface
The Gnielinski correction is applied for temperature analysis
  Current model dimensionless number
    Re ~ 10560
    Pr ~ 7
  Details in “N:\leeg\Presentation\ LPCS_drift_tube_transient”